OpenEXR File Layout
Last Update: Aug 5, 2011
Florian Kainz
Industrial Light & Magic
# Document Purpose and Audience
This document gives an overview of the layout of OpenEXR 2.0 image files as byte sequences. It covers both single and multi-part formats, and how deep data is handled.
The text assumes that the reader is familiar with OpenEXR terms such as "channel", "attribute", "data window" or "chunk". For an explanation of those terms see the Technical Introduction to OpenEXR.
Note: This document does not define the OpenEXR file format. OpenEXR is defined as the file format that is read and written by the IlmImf open-source C++ library. If this document and the IlmImf library disagree, then the library takes precedence.

# Backwards Compatibility and New or Changed Functionality
## OpenEXR Backwards Compatibility (1.7 and 2.0)
OpenEXR 1.7 and earlier format files are fully supported by OpenEXR 2.0. You can still use the 1.7 file format with the 2.0 library. If you use the 2.0 format for single-part scan line image and tile image data, your data will be stored in the same way as the 1.7 files. You can recompile your 1.7 files to take advantage of the new format EXRs (multiple-part files, and/or deep scan line and deep tile data).
## New Features for OpenEXR 2.0: Multi-Part and Deep Data
The multi-part format is an extension of the OpenEXR 1.7 single-part file format. In addition to supporting the OpenEXR 1.7 data storage (a single scan line or tiled image), OpenEXR 2.0 files can be used to store multiple views and/or deep data (deep scan line or deep tiles).
While you can continue to use the 1.7 format for files, these changes to the file layout are required to support the new multi-part and deep data features:
Feature	Description	See
Version field	Bits 11 and 12 indicate whether the file contains deep data (bit 11), or more than one part (bit 12).	Deep Data on page 6
Header	To store more than one part in the file, you need to have a header for each part.	Structure on page 7
Header attributes	There are a number of attributes which have been defined to store data which is relevant to deep data and multi-part files. These include: name (one for each part), data type (you can have different types of data in different views), and the maximum number of samples to take in a deep data channel.	Multi-Part and Deep Data Header Attributes on page 9
Offset tables and chunks	To store more than one part in the file, you need to have an offset table for each part, and chunks for each part. / The chunks must begin with a part number.	Component Four: Offset Tables on page 10, and Chunk Layout on page 11.
Deep Data	Deep data has a unique storage format.	Deep Data on page 13

# Basic Data Types
An OpenEXR file is a sequence of 8-bit bytes. Groups of bytes represent basic objects such as integral numbers, floating-point numbers and text. Those objects are grouped together to form compound objects such as attributes or scan lines.
## Integers
Binary integral numbers with 8, 16, 32 or 64 bits are stored as 1, 2, 4 or 8 bytes. Integral numbers can be signed or unsigned. Signed numbers are represented using two's complement. Integral numbers are little-endian (that is, the least significant byte is closest to the start of the file).
OpenEXR uses the following six integer data types:
name	signed	size in bytes
unsigned char	no	1
short	yes	2
unsigned short	no	2
int	yes	4
unsigned int	no	4
unsigned long	no	8

## Floating-Point Numbers
Binary floating-point numbers with 16, 32 or 64 bits are stored as 2, 4 or 8 bytes. The representation of 32-bit and 64-bit floating-point numbers conforms to the IEEE 754 standard. The representation of 16-bit floating-point numbers is analogous to IEEE 754, but with 5 exponent bits and 10 bits for the fraction. The exponent bias is 15. Floating-point numbers are little-endian (that is: the least significant bits of the fraction are in the byte closest to the beginning of the file, while the sign bit and the most significant bits of the exponent are in the byte closest to the end of the file).
The following table lists the names and sizes of OpenEXR's floating-point data types:
name	size in bytes
half	2
float	4
double	8

## Text
Text strings are represented as sequences of 1-byte characters of type char. Depending on the context, either the end of a string is indicated by a null character (0x00), or the length of the string is indicated by an int that precedes the string.
## Packing
Data in an OpenEXR file are densely packed; the file contains no "padding". For example, consider the following C struct:
struct SI
{
   short s;
   int i;
};
On most computers, the in-memory representation of an SI object occupies 8 bytes: 2 bytes for s, 2 padding bytes to ensure four-byte alignment of i, and 4 bytes for i. In an OpenEXR file the same object would consume only 6 bytes: 2 bytes for s and 4 bytes for i. The 2 padding bytes are not stored in the file.
# File Layout
## High-Level Layout
Depending on whether the pixels in an OpenEXR file are stored as scan lines or as tiles, the file consists of the following components:
component	single-part file with...		multi-part file:
	scan lines:	tiles:
one	magic number	magic number	magic number
two	version field	version field	version field
three	header	header	part 0 header / [part 1 header] / ... / [<empty header>]
four	line offset table	tile offset table	part 0 chunk offset table / [part 1 chunk offset table] / ...
five	scan line blocks	tiles	chunks

It is the version field part which indicates whether the file is single or multi-part and whether the file contains deep data. “Chunk” is a general term to describe blocks of pixel data. A chunk can be a scan line block, a tile or deep data (scan line or tile).
Deep data has no unique component structure of its own, but uses the structure that the file would have if it did not have deep data in it.
## Comparison between Single-Part and Multi-Part File Layouts
Multi-part files have the same high level structure as single-part OpenEXR files, except the header, offset table and chunk components can have any number (two or more) parts. There must be the same number of headers as offset tables, and they must be in the same order. In addition, the header component of a multi-part file must end with a null byte (0x00). In multi-part files, each chunk contains a field that indicates which part's data it contains.
# Components One and Two: Magic Number and Version Field
## Magic Number
The magic number, of type int, is always 20000630 (decimal). It allows file readers to distinguish OpenEXR files from other files, since the first four bytes of an OpenEXR file are always 0x76, 0x2f, 0x31 and 0x01.
## Version Field
The version field, of type int, is the four-byte group following the magic number, and it is treated as two separate bit fields.
Byte/bit position	Description and notes
first byte (bits 0 through 7)	The 8 least significant bits, they contain the file format version number. / The current OpenEXR version number is version 2.
second, third and fourth bytes (bits 8 through 31)	The 24 most significant bits, these are treated as a set of boolean flags. / Bit 9 (the single tile bit) / bit mask: 0x200 Indicates that this is a single-part file which is in tiled format. If bit 9 is 1: / this is a regular single-part image and the pixels are stored as tiles, and / bits 11 and 12 must be 0. / If bit 9 is 0, and bits 11 and 12 are also 0: the data is stored as regular single-part scan line file. / This bit is for backwards compatibility with older libraries: it is only set when there is one "normal" tiled image in the file. / Bit 10 (the long name bit) / bit mask: 0x400 Indicates whether the file contains “long names”. If bit 10 is 1, the maximum length is 255 bytes. / If bit 10 is 0, the maximum length of attribute names, attribute type names and channel names is 31 bytes. / Bit 11 (the non-image bit) / bit mask: 0x800 Indicates whether the file contains any “non-image parts” (deep data). If bit 11 is 1, there is at least one part which is not a regular scan line image or regular tiled image (that is, it is a deep format). / If bit 11 is 0, all parts are entirely single or multiple scan line or tiled images. / New in 2.0. / Bit 12 (the multipart bit) / bit mask: 0x1000 Indicates the file is a multi-part file. If bit 12 is 1: / the file does not contain exactly 1 part and the 'end of header' byte must be included at the end of each header part, and / the part number fields must be added to the chunks. / If bit 12 is 0, this is not a multi-part file and the 'end of header' byte and part number fields in chunks must be omitted. / New in 2.0. / The remaining 19 flags in the version field are currently unused and should be set to 0.

### Version field, valid values
All valid combinations of the version field bits are as follows:
Description	Compatible with	bit 9	bit 10	bit 11
Single-part scan line. One normal scan line image.	All versions of OpenEXR.	0	0	0
Single-part tile. One normal tiled image.	All versions of OpenEXR.	1	0	0
Multi-part (new in 2.0). Multiple normal images (scan line and/or tiled).	OpenEXR 2.0.	0	0	1
Single-part deep data (new in 2.0). One deep tile or deep scan line part.	OpenEXR 2.0.	0	1	0
Multi-part deep data (new in 2.0). Multiple parts (any combination of: tiles, scan lines, deep tiles and/or deep scan lines).	OpenEXR 2.0.	0	1	1

Note: The version field bits define what capabilities must be available in the software so it can handle the file, rather than the exact format of the file. While the 9 and 11 bit settings must agree with the type attributes of all parts, in OpenEXR 2.0 the data format of each type is definitively set by the type attribute in that part's header alone.
# Component Three: Header
## Structure
### Single-part file
The header component of the single-part file holds a single header (for single-part files).
Each header is a sequence of attributes ended by a null byte.
The file has the same structure as a 1.7 file. That is, the multi-part bit (bit 12) must be 0, and the single null byte that signals the end of the headers must be omitted. This structure also applies to single-part deep data files.
### Multi-part file (new in 2.0)
The header component of a multi-part file holds a set of headers, with a separate header for each part (in multi-part files) and a null byte signalling the end of the header component:
part 0 header / [part 1 header] / ... / [<empty header>]

Each header is a sequence of attributes ended by a null byte.
The multipart bit (bit 12) must be set to 1, and the list of headers must be followed by a single null byte (0x00) (that is, an empty header).
## Attribute Layout
The layout of an attribute is as follows:
attribute name
attribute type
attribute size
attribute value

The attribute name and the attribute type are null-terminated text strings. Excluding the null byte, the name and type must each be as least 1 byte and at most :
- 31 bytes long (if bit 10 is set to 0), or
- 255 bytes long (if bit 10 is set to 1).
Both single-part and multi-part files use the same attribute types.
The attribute size, of type int, indicates the size (in bytes) of the attribute value.
The layout of the attribute value depends on the attribute type. The IlmImf library predefines several different attribute types (see page 14). Application programs can define and store additional attribute types.
## Header Attributes (All Files)
The header of every OpenEXR file must contain at least the following attributes:
attribute name	attribute type
channels	chlist
compression	compression
dataWindow	box2i
displayWindow	box2i
lineOrder	lineOrder
pixelAspectRatio	float
screenWindowCenter	v2f
screenWindowWidth	float

For descriptions of what these attributes are for, see the Technical Introduction to OpenEXR.
## Tile Header Attribute
This attributes is required in the header for all files which contain one or more tiles:
attribute name	attribute type	Notes
tiles	tiledesc	Determines the size of the tiles and the number of resolution levels in the file. / Note: The IlmImf library ignores tile description attributes in scan line based files. The decision whether the file contains scan lines or tiles is based on the value of bit 9 in the file's version field, not on the presence of a tile description attribute.

## Multi-View Header Attribute
This attribute can be used in the header for multi-part files:
attribute name	attribute type	Notes
view	text

## Multi-Part and Deep Data Header Attributes (New in 2.0)
These attributes are required in the header for all multi-part and/or deep data OpenEXR files.
attribute name	attribute type	Notes
name	string	Required if either the multipart bit (12) or the non-image bit (11) is set.
type	string	Required if either the multipart bit (12) or the non-image bit (11) is set. / Set to one of: / scanlineimage / tiledimage / deepscanline, or / deeptile. / Note: This value must agree with the version field's tile bit (9) and non-image (deep data) bit (11) settings.
version	int	This document describes version 1 data for all part types. / version is required for deep data (deepscanline and deeptile) parts. If not specified for other parts, assume version=1.
chunkCount	int	Required if either the multipart bit (12) or the non-image bit (11) is set.
tiles	tileDesc	Required for parts of type tiledimage and deeptile.

For more information about the standard OpenEXR attributes and optional attributes such as preview images, see the OpenEXR File Layout document.
## Deep Data Header Attributes (New in 2.0)
These attributes are required in the header for all files which contain deep data (deepscanline or deeptile):
attribute name	attribute type	Notes
tiles	tileDesc	Required for parts of type tiledimage and deeptile.
maxSamplesPerPixel	int	Required for deep data (deepscanline and deeptile) parts. / Note: Since the value of maxSamplesPerPixel maybe be unknown at the time of opening the file, the value “-1” is written to the file to indicate an unknown value. When the file is closed, this will be overwritten with the correct value. If file writing does not complete correctly due to an error, the value -1 will remain. In this case, the value must be derived by decoding each chunk in the part.
version	int	Should be set to 1. It will be changed if the format is updated.
type	string	Must be set to deepscanline or deeptile.

For information about channel layout and a list of reserved channel names, see the Technical Introduction to OpenEXR document, Channel Names section.
# Component Four: Offset Tables
## Offset Tables
An offset table allows random access to pixel data chunks. An offset table is a sequence of offsets, with one offset per chunk. Each offset (of type unsigned long) indicates the distance, in bytes, between the start of the file and the start of the chunk.
Chunks can be of any of the four data types.
## Offset Table Size
The number of entries in an offset table is defined in one of two ways:
1. If the multipart (12) bit is unset and the chunkCount is not present, the number of entries in the chunk table is computed using the dataWindow and tileDesc attributes and the compression format.
2. If the multipart (12) bit is set, the header must contain a chunkCount attribute (which indicates the size of the table and the number of chunks).
## Scan Lines
For scan line blocks, the line offset table is a sequence of scan line offsets, with one offset per scan line block. In the table, scan line offsets are ordered according to increasing scan line y coordinates.
## Tiles
For tiles, the offset table is a sequence of tile offsets, one offset per tile. In the table, scan line offsets are sorted the same way as tiles in INCREASING_Y order.
## Multi-part (New in 2.0)
For multi-part files, each part defined in the header component has a corresponding chunk offset table.
# Component Five: Pixel data
## Chunk Layout (New in 2.0)
A “chunk” is a general term for a pixel data block. The scan line and tile images have the same format that they did in OpenEXR 1.7. OpenEXR 2.0 introduces two new types (deep scan line and deep tile).
The layout of each chunk is as follows:
[part number] (if multi-part bit is set)
chunk data

The part number (of type unsigned long) is only present in multi-part files. It indicates which part this chunk belongs to. 0 indicates the chunk belongs to the part defined by the first header and the first chunk offset table. The part number is omitted if the multi-part bit (12) is not set (this saves space and enforces backwards compatibility to software which does not support multi-part files).
The chunk data is dependent on the type attribute - but (other than the part number) has the same structure as a single-part file of the same format:
part type	type attribute	Notes
scan line	indicated by a type attribute of “scanlineimage”	Each chunk stores a scan line block, with the minimum y coordinate of the scan line(s) within the chunk. / See Regular scan line image block layout, on page 12.
tiled	indicated by a type attribute of “tiledimage”	See Regular image tile layout, on page 12.
deep scan line	indicated by a type attribute of “deepscanline”	See Deep scan line layout, on page 13.
deep tile	indicated by a type attribute of “deeptile”	See Deep tiled layout, on page 13.

For more information about data types, see page Error: Reference source not found.
## Regular Scan Line Blocks
For scan line images and deep scan line images, one or more scan lines may be stored together as a scan line block. The number of scan lines per block depends on how the pixel data are compressed:
compression method	number of scan lines per block
NO_COMPRESSION	1
RLE_COMPRESSION	1
ZIPS_COMPRESSION	1
ZIP_COMPRESSION	16
PIZ_COMPRESSION	32
PXR24_COMPRESSION	16
B44_COMPRESSION	32
B44A_COMPRESSION	32

Each scan line block has a y coordinate of type int. The block's y coordinate is equal to the pixel space y coordinate of the top scan line in the block. The top scan line block in the image is aligned with the top edge of the data window (that is, the y coordinate of the top scan line block is equal to the data window's minimum y).
If the height of the image's data window is not a multiple of the number of scan lines per block, then the block that contains the bottom scan line contains fewer scan lines than the other blocks.
### Regular scan line image block layout
The layout of a regular image scan line block is as follows:
[part number] (if multipart bit is set)
y coordinate
pixel data size
pixel data

The pixel data size, of type int, indicates the number of bytes occupied by the actual pixel data.
Within the pixel data, scan lines are stored top to bottom. Each scan line is contiguous, and within a scan line the data for each channel are contiguous. Channels are stored in alphabetical order, according to channel names. Within a channel, pixels are stored left to right.
### Compressed data
If the file's compression method is NO_COMPRESSION, then the original, uncompressed pixel data are stored directly in the file. Otherwise, the uncompressed pixels are fed to the appropriate compressor, and either the compressed or the uncompressed data are stored in the file, whichever is smaller.
The layout of the compressed data depends on which compression method was applied. The compressed formats are not described here. For information on the compressed data formats, see the source code for the IlmImf library.
## Regular ImageTiles
### Regular image tile layout
The layout of a regular image tile is as follows:
[part number] (if multi-part bit is set)
tile coordinates
pixel data size
pixel data

The tile coordinates, a sequence of four ints (tileX, tileY, levelX, levelY) indicates the tile's position and resolution level. The pixel data size, of type int, indicates the number of bytes occupied by the pixel data.
The pixel data in a tile are laid out in the same way as in a scan line block, but the length of the scan lines is equal to the width of the tile, and the number of scan lines is equal to the height of the tile.
If the width of a resolution level is not a multiple of the file's tile width, then the tiles at the right edge of that resolution level have shorter scan lines. Similarly, if the height of a resolution level is not a multiple of the file's tile height, then tiles at the bottom edge of the resolution level have fewer scan lines.
## Deep Data (New in 2.0)
Deep images store an arbitrarily long list of data at each pixel location (each pixel contains a list of samples, and each sample contains a fixed number of channels).
### Deep scan line layout
Deep scan line images are indicated by a type attribute of “deepscanline”. Each chunk of deep scan line data is a single scan line of data. The data in each chunk is laid out as follows:
[part number] (if multipart bit is set)
y coordinate
packed size of pixel offset table
packed size of sample data
unpacked size of sample data
compressed pixel offset table
compressed sample data

The unpacked size of the sample data (an unsigned long) is the size of the deep sample data once it is unpacked. It is necessary to specify the unpacked size since the data may be arbitrarily large (so generally cannot otherwise be determined without decompressing the data first).
### Deep tiled layout
Tiled images are indicated by a type attribute of “deeptile”. Each chunk of deep tile data is a single tile. The data in each chunk is laid out as follows:
[part number] (if multipart bit is set)
tile coordinates
packed size of pixel offset table
packed size of sample data
unpacked size of sample data
compressed pixel offset table
compressed sample data

The unpacked size of the sample data (an unsigned long) is the size of the deep data once it is unpacked. It is necessary to specify the unpacked size since the data may be arbitrarily large (so generally cannot otherwise be determined without decompressing the data first).
The pixel offset table is a list of ints, one for each column within the dataWindow. Each entry n in the table indicates the total number of samples required to store the pixel in n as well as all pixels to the left of it. Thus, the first samples stored in each channel of the pixel data are for the pixel in column 0, which contains table[1] samples. Each channel contains table[width-1] samples in total.
### Unpacked deep data chunks
When decompressed, the unpacked chunk consists of the channel data stored in a non-interleaved fashion:
pixel sample data for channel 0 / pixel sample data for channel 1 / pixel sample data for channel ... / pixel sample data for channel n

Exception: For ZIP_COMPRESSION only there will be up to 16 scanlines in the packed sample data block:
pixel sample data for channel 0 for scanline 0 / pixel sample data for channel 1 for scanline 0 / pixel sample data for channel ... for scanline 0 / pixel sample data for channel n for scanline 0 / pixel sample data for channel 0 for scanline 1 / pixel sample data for channel 1 for scanline 1 / pixel sample data for channel ... for scanline 1 / pixel sample data for channel n for scanline 1 / ...

### Deep data compression
The following compression schemes are the only ones permitted for deep data:
compression method	number of scan lines per block
NO_COMPRESSION	1
RLE_COMPRESSION	1
ZIPS_COMPRESSION	1
ZIP_COMPRESSION	16

# Predefined Attribute Types
The IlmImf library predefines the following attribute types:
type name	data
box2i	Four ints: xMin, yMin, xMax, yMax
box2f	Four floats: xMin, yMin, xMax, yMax
chlist	A sequence of channels followed by a null byte (0x00). / Channel layout: / name zero-terminated string, from 1 to 255 bytes long / pixel type int, possible values are: / UINT = 0 / HALF = 1 / FLOAT = 2 / pLinear unsigned char, possible values are 0 and 1 / reserved three chars, should be zero / xSampling int / ySampling int
chromaticities	Eight floats: redX, redY, greenX, greenY, blueX, blueY, whiteX, whiteY
compression	unsigned char, possible values are / NO_COMPRESSION = 0 / RLE_COMPRESSION = 1 / ZIPS_COMPRESSION = 2 / ZIP_COMPRESSION = 3 / PIZ_COMPRESSION = 4 / PXR24_COMPRESSION = 5 / B44_COMPRESSION = 6 / B44A_COMPRESSION = 7
double	double
envmap	unsigned char, possible values are: / ENVMAP_LATLONG = 0 / ENVMAP_CUBE = 1
float	float
int	int
keycode	Seven ints: filmMfcCode, filmType, prefix, count, perfOffset, perfsPerFrame, perfsPerCount
lineOrder	unsigned char, possible values are: / INCREASING_Y = 0 / DECREASING_Y = 1 / RANDOM_Y = 2
m33f	9 floats
m44f	16 floats
preview	Two unsigned ints, width and height, followed by 4×width×height unsigned chars of pixel data. / Scan lines are stored top to bottom; within a scan line pixels are stored from left to right. A pixel consists of four unsigned chars, R, G, B, A.
rational	An int, followed by an unsigned int.
string	String length, of type int, followed by a sequence of chars.
stringvector	A sequence of zero or more text strings. Each string is represented as a string length, of type int, followed by a sequence of chars. The number of strings can be inferred from the total attribute size (see the Attribute Layout section, on page 8).
tiledesc	Two unsigned ints: xSize, ySize, followed by mode, of type unsigned char, where / mode = levelMode + roundingMode×16 / Possible values for levelMode: / ONE_LEVEL = 0 / MIPMAP_LEVELS = 1 / RIPMAP_LEVELS = 2 / Possible values for roundingMode: / ROUND_DOWN = 0 / ROUND_UP = 1
timecode	Two unsigned ints: timeAndFlags, userData.
v2i	Two ints
v2f	Two floats
v3i	Three ints.
v3f	Three floats.

# Sample File
The following is an annotated byte-by-byte listing of a complete OpenEXR file. The file contains a scan-line based image with four by three pixels. The image has two channels: G, of type HALF, and Z, of type FLOAT. The pixel data are not compressed. The entire file is 415 bytes long.
The first line of text in each of the gray boxes below lists up to 16 bytes of the file in hexadecimal notation. The second line in each box shows how the bytes are grouped into integers, floating-point numbers and text strings. The third and fourth lines indicate how those basic objects form compound objects such as attributes or the line offset table.

76 2f 31 01 02 00 00 00 63 68 61 6e 6e 65 6c 73
20000630 | 2 | c h a n n e l s
magic number | version, flags | attribute name
| | start of header

00 63 68 6c 69 73 74 00 25 00 00 00 47 00 01 00
\0 | c h l i s t \0 | 37 | G \0 | HALF
| attribute type | attribute size | attribute value

00 00 00 00 00 00 01 00 00 00 01 00 00 00 5a 00
| 0 | 0 | 1 | 1 | Z \0 |

02 00 00 00 00 00 00 00 01 00 00 00 01 00 00 00
FLOAT | 0 | 0 | 1 | 1 |
|

00 63 6f 6d 70 72 65 73 73 69 6f 6e 00 63 6f 6d
\0 | c o m p r e s s i o n \0 | c o m
| attribute name | attribute type

70 72 65 73 73 69 6f 6e 00 01 00 00 00 00 64 61
p r e s s i o n \0 | 1 | NONE| d a
| attribute size |value|

74 61 57 69 6e 64 6f 77 00 62 6f 78 32 69 00 10
t a W i n d o w \0 | b o x 2 i \0 |
attribute name | attribute type |

00 00 00 00 00 00 00 00 00 00 00 03 00 00 00 02
16 | 0 | 0 | 3 |
attribute size| attribute value

00 00 00 64 69 73 70 6c 61 79 57 69 6e 64 6f 77
2 | d i s p l a y W i n d o w
| attribute name

00 62 6f 78 32 69 00 10 00 00 00 00 00 00 00 00
\0 | b o x 2 i \0 | 16 | 0 |
| attribute type | attribute size | attribute value

00 00 00 03 00 00 00 02 00 00 00 6c 69 6e 65 4f
0 | 3 | 2 | l i n e O
| attribute name

72 64 65 72 00 6c 69 6e 65 4f 72 64 65 72 00 01
r d e r \0 | l i n e O r d e r \0 |
| attribute type |

00 00 00 00 70 69 78 65 6c 41 73 70 65 63 74 52
1 |INCY | p i x e l A s p e c t R
attribute size|value| attribute name

61 74 69 6f 00 66 6c 6f 61 74 00 04 00 00 00 00
a t i o \0 | f l o a t \0 | 4 |
| attribute type | attribute size |

00 80 3f 73 63 72 65 65 6e 57 69 6e 64 6f 77 43
1.0 | s c r e e n W i n d o w C
attribute value| attribute name

65 6e 74 65 72 00 76 32 66 00 08 00 00 00 00 00
e n t e r \0 | v 2 f \0 | 8 |
| attribute type | attribute size |

00 00 00 00 00 00 73 63 72 65 65 6e 57 69 6e 64
0.0 | 0.0 | s c r e e n W i n d
attribute value | attribute name

6f 77 57 69 64 74 68 00 66 6c 6f 61 74 00 04 00
o w W i d t h \0 | f l o a t \0 |
| attribute type |

00 00 00 00 80 3f 00 3f 01 00 00 00 00 00 00 5f
4 | 1.0 | \0 | 319 |
size | attribute value | | offset of scan line 0 |
end of header | start of scan line offset table

01 00 00 00 00 00 00 7f 01 00 00 00 00 00 00 00
351 | 383 |
offset of scan line 1 | offset of scan line 2 |
end of scan line offset table |

00 00 00 18 00 00 00 00 00 54 29 d5 35 e8 2d 5c
0 | 24 | 0.000 | 0.042 | 0.365 | 0.092 |
y | pixel data size | pixel data for G channel |
scan line 0

28 81 3a cf e1 34 3e 8b 0b bb 3d 89 74 f9 3e 01
0.000985395 | 0.176643 | 0.0913306 | 0.487217 |
pixel data for Z channel |
|

00 00 00 18 00 00 00 37 38 76 33 74 3b 73 38 7f
1 | 24 | 0.527 | 0.233 | 0.932 | 0.556 |
y | pixel data size | pixel data for G channel |
scan line 1

ab e8 3e 8a cf 54 3f 5b 6c 11 3f 20 35 50 3d 02
0.454433 | 0.831292 | 0.56806 | 0.0508319 |
pixel data for Z channel |
|

00 00 00 18 00 00 00 23 3a 0a 34 02 3b 5d 3b 38
2 | 24 | 0.767 | 0.252 | 0.876 | 0.920 |
y | pixel data size | pixel data for G channel |
scan line 2

f3 9a 3c 4d ad 98 3e 1c 14 08 3f 4c f3 03 3f
0.0189148 | 0.298197 | 0.531557 | 0.515431
pixel data for Z channel
end of file